## Slide 1: Prairie 1 microscope
RH 230111

## Slide 2: Spirit: Photo-Stimulation Laser-Path
Spirit (SpectraPhysics)
(1040 nm)
Outside
Inside
SLM path
Uncaging path
Component Details
Spirit Spectra-Physics Laser λ = 1040nm, τ = 300fs, P <9W
(Focusing?) Telescope Lens 1: ???, Lens 2: ???
Pockels Cell? Lasermetrics
(details obscured…)
Polarizer Prism (XXX) in SM1PM10 mount (Thorlabs)
Dichroic mirror
(Specifications lacking)
Half-Wave Plate
(specifications)
Flip mirror for either stimulation path

## Slide 3: Chameleon Coherent: Imaging Laser-Path
Chameleon Coherent
Component Details
Expanding Telescope Lens 1: f = 125mm, Lens 2: f = 400mm
Chameleon Coherent Tunable Laser λ = 920nm….
Chameleon Coherent
Outside
Inside
Imaging path
Electrotunable Lens (ETL) Specifications: XXXX
Alternative path
to SLM
Two Flip-In mirrors to direct Imaging Laser for SLM-path

## Slide 4: Output paths
SLM path (Im. + Stim.)
Uncaging path
Imaging path (post-ETL)
sidebox
Main Prairie-box
Component Details
Expanding Telescope (650-1050nm) Lens 1: 200mm, Lens 2: 50mm
Dichroic mirror
SP1030
25x
Flip-mirrors
1) Stim-path, 2) SLM-path flip-in
SLM 512x512 MeadowLark
Extra Fat Mirrors
Galvo-Galvo mirrors
Resonant Galvo mirrors
Fat Final Lens
f = 400mm